## Slide 1: TE IT Computer Network Technology
Prof. M.R.Mahajan

## Slide 2: Unit 6: RECENT TRENDS IN COMMUNICATION NETWORKS
Satellite Network
Wireless Sensor Network
Computational Grid
Internet of Things
Software Defined Network
Network Function Virtualization
Network Neutrality

## Slide 3: Satellite Network
A satellite is an object that revolves around another object.
  E.g. moon is a satellite of earth
A communication satellite is a microwave repeater station in a space that is used for telecommunication, radio and television signals.
A communication satellite processes the data coming from one earth station and it converts the data into another form and send it to the second earth station.

## Slide 4: Satellite Network
How a Satellite Works:
Fig: Satellite Communication for Internet Data Movement

## Slide 5
How a Satellite Works:
  Two stations on earth want to communicate through radio broadcast but are too far away to use conventional means.
  The two stations can use a relay station for their communication.
  One earth station transmits the signal to the satellite.
  Uplink frequency:-
    Frequency at which ground station is communicating with satellite.
  Downlink frequency:-
    Frequency at which satellite transponder converts the signal and sends it down to the second earth station

## Slide 6: Advantages & Disadvantages of Satellite
Advantages :
  The Coverage area is very high.
  Versatile, Fast, Expandable, Flexible, Universal
  Higher bandwidths are possible.
Advantages :
  Launching satellites into orbits is a costly process.
  The bandwidths are gradually used up.
  High signal propagation delay.

## Slide 7: Types of Earth Orbit Satellites
Geosynchronous Earth Orbit Satellites (GEO)
  Geostationary Earth Orbit Satellites
Medium Earth Orbit Satellites (MEO)
Low Earth Orbit Satellites (LEO)

## Slide 8: Geosynchronous Earth Orbit Satellite (GEO )
Placed at an altitude of 22,300 miles (36000 km) above the Earth
This orbit is synchronized with a side real day (i.e., 23hours 56minutes and 4 Second)
This orbit can have inclination and eccentricity
Geo-synchronous orbit, if it is circular and in the plane of equator, it is called as geo-stationary orbit
Use:
weather forecasting,
satellite TV,
satellite radio
other types of global communications

## Slide 9: Medium Earth Orbit Satellite (MEO )
MEO satellite networks will orbit at distances of about 8000 miles from earth's surface
Signals travel a shorter distance.
Orbital periods range from about 2 to 24 hours
Improved signal strength is travelling a shorter distance to and from the satellite, there is less transmission delay.
Use:
  Global Positioning System (GPS)
  E.g.: Telstar, one of the first and most famous experimental satellites, orbits in MEO

## Slide 10: Low Earth Orbit Satellite (LEO )
LEO has a circular orbit about 400 to 900 km above the earth’s surface.
LEO has a much shorter period (time to revolve around the earth) of about 90 minutes.
Because of their low altitude, these satellites are only visible from within a small area (about 1000 km radius)
LEO satellites are often part of a group of satellites working in concert.
Use:
  Local Applications
  E.g. Iridium (66 satellites; rent for
  global Iridium satellite phones is as low as $24.95 per week)

## Slide 11: Video: How Satellite Works
https://www.youtube.com/watch?v=ror4P1UAv_g

## Slide 12: References
http://wiki.cas.mcmaster.ca/index.php/Satellite_Networking
https://www.esoa.net/technology/satellite-orbits.asp
https://www.groundcontrol.com/How_Does_Satellite_Internet_Work.htm
https://www.tutorialspoint.com/wireless_communication/wireless_communication_satellite.htm
https://en.wikipedia.org/wiki/Satellite_Internet_access