## Slide 1: IP Addresses
An IPv4 address is a 32-bit address.
The address space of IPv4 is 232 or 4,294,967,296.

## Slide 2
IP addresses, when started a few decades ago, used the concept of classes. This architecture is called classful addressing. In the mid-1990s, a new architecture, called classless addressing, was introduced and will eventually surpass the original architecture. However, part of the Internet is still using classful addressing, but the migration is very fast.

## Slide 3
Classful Addressing

## Slide 4
Class A | 0-127 | n/w . Host . Host . Host
Class B | 128-191 | n/w . n/w . Host . Host
Class C | 192-223 | n/w . n/w . n/w . Host
Class D | 224-239 | Multicast addresses
Class E | 240-255 | Reserved for future use

## Slide 5: Occupation of the address space

## Slide 6
Find the class of each address:
227.12.14.87
193.14.56.22
14.23.120.8
252.5.15.111
134.11.78.56

## Slide 7: Blocks in class A
10.0.0.0 – 10.255.255.255 is used for private addresses

## Slide 8: Blocks in class B
Total 16 blocks, 172.16.0.0 – 172.31.255.255 used for private addresses

## Slide 9: Blocks in class C
Total 255 blocks, 192.168.0.0 – 192.168.255.255 used for private addresses

## Slide 10
Given the network addresses, find the class, the block, and the range of the addresses.
17.0.0.0
132.21.0.0
220.34.76.0

## Slide 11: Masking
To find Netid from given address
Ex.
200.45.34.56 11001000 00101101 00100010 00111000
255.255.255.0 11111111 11111111 11111111 00000000
200.45.34.0 11001000 00101101 00100010 00111000

## Slide 12
Default masks

## Slide 13
Given the addresses, find the beginning address (network address).
23.56.7.91
132.6.17.85
201.180.56.5

## Slide 14: Special addresses

## Slide 15
Network address

## Slide 16
direct broadcast address

## Slide 17
limited broadcast address

## Slide 18
this host on this network

## Slide 19
specific host on this network

## Slide 20
loopback address

## Slide 21: SUBNETTING AND SUPERNETTING
The network addresses available for assignment to organizations are close to depletion. This is coupled with the ever-increasing demand for addresses from organizations that want connection to the Internet.
two solutions: subnetting and supernetting.

## Slide 22
IP addresses are designed with two levels of hierarchy

## Slide 23: Addresses in a network with and without subnetting

## Slide 24: Default mask and subnet mask

## Slide 26
What is the subnetwork address if the destination address is 200.45.34.56 and the subnet mask is 255.255.240.0?
Address ➡ 11001000 00101101 00100010 00111000
Subnet Mask ➡ 11111111 11111111 11110000 00000000
Subnetwork Address ➡ 11001000 00101101 00100000 00000000.

## Slide 27: Comparison of subnet, default, and supernet masks

## Slide 28
Note:
The idea of subnetting and supernetting of classful addresses is almost obsolete.

## Slide 29
Classless Addressing
In classless addressing variable-length blocks are assigned that belong to no class. In this architecture, the entire address space (232 addresses) is divided into blocks of different sizes.

## Slide 30
Subnetting
When an organization is granted a block of addresses, it can create subnets to meet its needs. The prefix length increases to define the subnet prefix length.
Fixed-Length Subnets
Variable-Length Subnets

## Slide 31
An organization is granted the block 130.34.12.64/26. Find first address, no of host and last address.
Example 1
The organization needs 4 subnets. What is the subnet prefix length? What are the subnet addresses and the range of addresses for each subnet.

## Slide 33
An organization is granted a block of addresses with the beginning address 14.24.74.0/24. There are 232−24= 256 addresses in this block. The organization needs to have 11 subnets as shown below:
a. two subnets, each with 64 addresses.
b. two subnets, each with 32 addresses.
c. three subnets, each with 16 addresses.
d. four subnets, each with 4 addresses.
Design the subnets.
Example 2

## Slide 35
An ISP is granted a block of addresses starting with 190.100.0.0/16 (65,536 addresses). The ISP needs to distribute these addresses to three groups of customers as follows:
Example 3
a. The first group has 64 customers; each needs 256 addresses. b. The second group has 128 customers; each needs 128 addresses c. The third group has 128 customers; each needs 64 addresses.
Design the subblocks and find out how many addresses are still available after these allocations.